# Parking capacity to support a ferry terminal location at or near the foot of University Avenue

Spaces	Location

25	Circle at end of Spinnaker Way, Cesar Chavez Park

77	Northside Launch Ramp, Cesar Chavez Park

161	A-E Docks and overflow for Cesar Chavez Park

495	Doubletree Hotel

105	East Side of Marina Docks F-I

200	South Sailing Basin Windsurfing area

105	J - K Dock Docks J-K, Marina Adm. Bldg, Bait Shop

115	Southside Cal Sailing and Cal Adventures

220	L - M Dock Docks L-M, Berkeley Co., Corporation Yard

133	Skates Restaurant Skates, Horseshoe Park

87	N - O Docks, Yacht Club

320	HS Lordships Rest. HS Lordships, Shorebird Park Spinnaker Way

65	On-street Cesar Chavez Park

90	Seawall Drive (End of University Ave South of Berkeley Pier)

Total:	2,198

SOURCE: Berkeley Marina Master Plan, Revised Draft 4/3/03.

Spaces that would directly serve a ferry terminal at the Berkeley Pier:

Hs. Lordships:  	320

Seawall Drive:  	  90

L-M docks        	220

Skates            	133

Total:              	763

In addition there are about 200 spaces of viable overflow parking at the South Sailing Basin, and 87 spaces at N and O-docks, although these will require another minute or two of walking.

Summary: There are about 1,000 spaces that could realistically serve passengers on the Berkeley Ferry. Hourly service by a 149-passenger ferry, assuming 80% arrive by car (from WTA study) and assuming that all cars are single-occupancy (worst case, neglecting multiple-passenger vehicles and "kiss-and-ride" drop-offs) and assuming full boats on three departures, results in an upper bound for parking demand of 358 spaces over the morning commute. Without these worst-case assumptions, the actual parking demand probably drops to somewhere around 300 spaces or less.

To avoid negative impacts on Skates and Hs. Lordships, it may be desirable to designate some spaces as 2-hour time limit for restaurant customers.

There appears to be no practical alternative for incorporating dedicated ferry parking. Multi-use is critical. The spaces used by ferry passengers during commute and working hours will be needed by restaurant customers in the evenings and Marina users on weekends.

A parking fee is desirable from a transportation planning point of view, but the close proximity of numerous other parking areas and the reliance by businesses, organizations and Marina users on these parking areas for all-day parking will make this very impractical. The same economic incentive can be achieved with a higher ticket price and a deep discount for bus transfers or bicycle riders.

# Text boxes

Aerial photo showing parking within 300 meters of a possible terminal location just south of the Municipal Fishing Pier (a 3.7 minute walk at 3 mph)